## Slide 1: BD EpiCenter™ WHONET Integration
Gurel SAHIN
EMA DMS & Instrument Expert
BD Diagnostics
gurel.sahin@bd.com
Jens Thomsen MD MPH
Chair, UAE Sub-Committee for AMR Surveillance
Abu Dhabi Public Health Center
Dept. of Health Abu Dhabi, UAE
jthomsen@doh.gov.ae

## Slide 2
+ Manual microbiology tests
  Microbiology Data Management Software designed to
    Improve the microbiology testing process
    Enhance microbiology result quality
    Conduct statistical / epidemiological analysis
    Under regulations of CE-IVD (Europe) and FDA (USA)
  BD EpiCenter Software can be directly interfaced to
    BD BACTEC™
    BD MGIT™
    BD Phoenix™
    BD Kiestra™
    Bruker Biotyper™
    and the HIS & LIS system
BD EpiCenterTM

## Slide 3
BD EpiCenterTM
Isolates and Resistance Markers
MIC Trend (Minimum – Average – Maximum)

## Slide 4
BD EpiCenterTM
Percent Susceptible Isolates (%S) Graph

## Slide 5
WHONET Data Export
  Four easy steps to sharing a data file that can be read by BacLink, and uploaded to WHONET:
  Launch Data View Module
  Generate a data file
  Convert the data file with BacLink
  Open WHONET and perform your analysis
5

## Slide 6
Launch BD EpiCenterTM (V6.60 or above) and log in
Select the “Data View” reporting module from the toolbar:
Step 1: Launch the DataView Module

## Slide 7
Select the predefined data filter in the following location:
    Predefined
      3-WHONET Data Export
        3-WHONET Data Export
  Press “Run”
Step 2: Generate a Data File for Export

## Slide 8
Enter the appropriate filter criteria to limit data returned:
  Beginning Collection Date
  Ending Collection Date
Press “Run”
Step 2: Generate a Data File for Export

## Slide 9
When the result data has been displayed:
Press “Print Preview”
Step 2: Generate a Data File for Export

## Slide 10
When the print preview screen has appeared, press the
  “Export” button
  located on top and then select the option to export data to
  “Tab separated text file”
File name and export file location will be suggested but could be modified before saving
Press “Save”
Step 2: Generate a Data File for Export

## Slide 11
Step 2: Generate a Data File for Export

## Slide 12
Step 3: Copy the Data File to the WHONET PC
Copy the data file onto a USB stick, then go to the WHONET computer, and save the data file into the folder:
C:\\WHONET\data
BD EpiCenter Computer
WHONET Computer

## Slide 13
STEP 3A: Setting up the data conversion (one time only):
Open BacLink and press:
“New format”
Step 3: Convert the File with BacLink

## Slide 14
Enter basic information:
  Country name
  Lab name (full name)
  Lab code (3 digits)
Press
  “File structure”
Step 3: Convert the File with BacLink

## Slide 15
For File structure select
  “BD EpiCenter”
Press
  “OK”, and
  “Save”
Step 3: Convert the File with BacLink

## Slide 16
Select a file name, e.g.
  “XYZ Hospital”
Press
  “Save”, then press
  “Exit”
Step 3: Convert the File with BacLink

## Slide 17
STEP 3B: Running the data conversion (repeat for each new data file):
For “File name”, select the BD EpiCenter data file
For “New data file” enter a file name, then press
“Begin conversion”
Step 3: Convert the File with BacLink

## Slide 18
Step 3: Convert the File with BacLink
BacLink shows the first isolate
Check the quality of the data conversion, including
  Length of fields
  Date formats
If ok, press: “Next” (3 times)
Otherwise press “Cancel”, and “Edit format” to modify settings

## Slide 19
BacLink will run through the data file, converting all data to a WHONET database file
Check the number of isolates in the data file for plausibility, then click
“OK”
Step 3: Convert the File with BacLink

## Slide 20
Step 3: Convert the File with BacLink
After the first conversion BACLINK might show a window, informing you that not all codes in the data file have been understood, and asking you if you want to review new codes.
For all data to be included in the WHONET file you should review the new codes, and as such click on “Yes”.

## Slide 21
Step 3: Convert the File with BacLink
In the next window BacLink shows the data fields that have unrecognized codes (here ‘Location’ and ‘Specimen Type’)
Click on ‘Location’ and then on ‘Define codes’ to define the unrecognized location codes (3SOUTH, 4 NORTH, 5NORTH, etc.)
Do the same for ‘Specimen type’
After defining all unrecognized codes, click on ‘Continue’ and ‘Begin conversion’ to run the conversion again

## Slide 22
Once all codes are defined press
  “OK”, and
  “Exit”
Step 3: Convert the File with BacLink

## Slide 23
Start WHONET and press “Cancel”
Step 4: Open the File with WHONET

## Slide 24
Click on
“File” and then
“Create a laboratory from a data file”
Step 4: Open the File with WHONET

## Slide 25
Enter “United Arab Emirates” for country, or as applicable
Enter Laboratory name and three digit code
Click on “Data files” and select the newly created WHONET file
Click on “OK”
Step 4: Open the File with WHONET
1.
2.
3.

## Slide 26
In the following screen click on “Yes” to review the laboratory configuration (this is optional)
Step 4: Open the File with WHONET

## Slide 27
In the “Laboratory configuration screen” you can review the laboratory configuration, including antibiotics, locations, data fields, and alerts, and modify them if needed.
Click on “Save” to save the newly created lab configuration.
Step 4: Open the File with WHONET

## Slide 28
The WHONET file is now ready for analysis.
To perform an analysis on this file click on “Data analysis” and “Data analysis” again
Then click on
  “Analysis type” to select the analysis type (e.g. “%RIS and test measurements”, and
  “Data files” to select the new file
  “Organisms” to select the organism (e.g. Staph. aureus), then click on
  “Begin analysis”
Step 4: Run the analysis with WHONET

## Slide 29
The analysis results screen should show something similar to this:
Review analysis results, then click on
“Continue” to proceed
Step 4: Run the analysis with WHONET

## Slide 30
For further details please refer to WHONET tutorial “BacLink 8.AST Vitek 2.English”
This tutorial can be found online at:
  www.whonet.org ( documents)
The file can also be found locally on the C: drive of your PC in the folder:
  C:\\WHONET\documents
Reference and further reading